## Slide 1: PC based Application

## Slide 2: Why
PC (IPC) is widely used in industries and business
  User friendly
  Powerful than embeded devices
  More general purpose
Embedded devices need PC applications to
  Control (operate)
  Config (set parameters, report status/warning/error...)
  Interactive (with people)

## Slide 3: Structure
Upper and lower System
PC
(Upper System)
MCU/Embedded
(Lower System)
Communication

## Slide 4: Example: DAQ Software
Data Aquisition
  Retrive data from embeded system
Software in PC Platform
  Interactive with user
  Show data in curve or form
  cooperate with lowersystem
Software in Embedded System
  data sample from sensor
  accept control command or config command from upper system
  push data to upper system

## Slide 5: Key part: Communication
Communication is how upper system to communicate with lower system
Tipical communication links include
  Ethernet
  Industry BUS
  Serial Port
Serial Communication
  Read/Write data bytes from/to serial port
  Both ends should follow the same protocol

## Slide 6: Serial Communication Protocol
Hardware protocol
  BaudRate
  Stop bits
  Data bits
  parity check (odd-even check)
Application protocol
  How bytes are used to present the actual physical value
  Using text may be simpler

## Slide 7: Text based protocol
Text-based Vs Binary-based
  Using text to present physical value is simple
  Text can adapt to all hardware platforms
  Text based protocol is low efficient, consuming more bandwidth
In DAQ system
  using text to present the actual value
  “0.01\n0.02\n0.03\n...”
  how to present complex data like (t, data)
  more complex data
    JSON
    XML
0.01
0.02
0.03
...
1, 0.01
2, 0.02
3, 0.03
...

## Slide 8: Serial communication in python
Using pySerial library
setup the serial communication parameters

## Slide 9
methods provided by pySerial
  ser.isOpen()：check if the port is open
  ser.open() ：open the port
  ser.close()：close the port
  ser.read()：read 1 byte from the port
  ser.read_all():read all bytes from the port
  ser.write()：write to the port
  ser.readline()：read a line from the port
  ser.readlines()：read multi-lines
  in_waiting()：wait for data come in
  flush()：send out all the data
  flushInput()：clear input buffer
  flushOutput()：clear output buffer

## Slide 10: Decode serial data
readline() to get the data in text form
parse the text into real data float(str)
If using complex form, using split() to split the data in text form before parse it.
print it on the screen (console)

## Slide 11: Write your own PC based software
Write a python program to repeatedly read data from serial port
Shoud be able to process exception
  port not open, port not exist, lower system is not ready, ...
Start lower system program first before run the program
  Lower system can be implemented using Arduino
  Arduino should write data to the serial port in the same text format
    using: Serial.println(data)
Keep test and make it robust
Write a report and turn in as a homework

## Slide 12: How to improve your program
Add GUI (Graphical User Interface)
With GUI, you can have more precise control to your program
  with start, stop button to start/stop the DAQ precess
  using curve to show the data instead of print to console
  let user config the serial port at run time
  visual feedback of the working status
More work will be need to design and implement the GUI
Using pyQt library or other library if you are familiar