## Slide 1: Practical software engineering for mechatronics systems
3: Advanced Knowledge About Arduino

## Slide 2: Arduino Basics
Program Structure
  setup() and loop()
Basic digital I/O, analog input and PWM output
  digitalRead() / digitalWrite()
  analogRead() / analogWrite()
Functions
  String, date, time, calculation, etc.
Serial communication

## Slide 3: Advanced topics
About Timer
How to use the arduino library
How to write your own library

## Slide 4: AT1: Timer
What is timer?
  Timer is a reminder that is strictly remind your code to do somthing at specified time instante.
Why Timer?
  Timer is very important in Real-time system.
  Generate a very presice time delay.
  Timer can work in backgroud / not comsuming CPU resources.

## Slide 5: AT1: Timer
Hardware Timer V.S. Software Timer
  Hardware timer usually available in CMU based system.
  Software timer usually available in PC based system.
  In Arduino, we use hardware Timer.
Hardware Timer
  2 timers in Arduino
  need to set the initial value, enable the interrupt
  do something in the interrupt service function

## Slide 6: Timer in Arduino
Hacker's way
  need knowlege about AVR MCU and C++
  hack into aruidno's codes to use C++ directly
  may NOT portable!
Smart-guy's way
  do it using library
  or
  do it using millis()

## Slide 7: AT2: Arduino Library
What is Arduino Library for?
  Provide extendable functions in addition to the basic library.
  A way to write BIG programs.
  Code re-use.
Where can I find the Arduino library?
How to use the library in my project?

## Slide 8: AT2: Arduino Library
What is Arduino Library for?
Where can I find the Arduino library?
  IDE
  Download from developers' website
  Write you own.
How to use the library in my project?
  Use IDE to include the library.

## Slide 9: AT3：How to write library
Using Class to encapsulate the source code
Essentially the library is a C++ class or package.
Put it into the library directory.

## Slide 10: Example: MsTimer2
/*
MsTimer2 is a small and very easy to use library to interface
Timer2 with humans. It's called MsTimer2 because it
"hardcodes" a resolution of 1 millisecond on timer2 For Details
see: http://www.arduino.cc/playground/Main/MsTimer2
*/
#include <MsTimer2.h>
// Switch on LED on and off each half second
#if ARDUINO >= 100
const int led_pin = LED_BUILTIN;// 1.0 built in LED pin var
#else
const int led_pin = 13; // default to pin 13
#endif
void flash()
{
static boolean output = HIGH;
digitalWrite(led_pin, output);
output = !output;
}
void setup()
{
pinMode(led_pin, OUTPUT);
MsTimer2::set(500, flash); // 500ms period
MsTimer2::start();
}
void loop()
{
}