## Slide 1: Arduino Basics
Dr. Xiaoming Li
(lxm@lxm.name)

## Slide 2: Outline
Know the board - facts
Arduino workflow
Software architecture for Arduino
Learn Arduino programming skills by examples

## Slide 3: Arduino the board
Credit card size
Full function
MCU-based
Easy to learn
Widely used in non-industrial fields, such as art, education, prototyping, etc.

## Slide 4: About the board
14 Digital I/O, programable
6 Analog Input
6 PWM output
1 UART
1 Reset button
1 USB, 1 Power jack
Onboard 5.5/3.3V
Onboard 4 LEDs
Microcontoller: ATmega328p

## Slide 5: How to use Arduino
Arduino is a computer
  Without Operation System
  Can only execute binary codes
  How to program
  How to execute
Host PC
Arduino
1 Coding/Compiling
2 Download program to Arduino
4 Interact through Serial Port
3 Running the program

## Slide 6: Arduino IDE
Download the installation file from http://www.arduino.cc
After installation, run the IDE
Configure the connection by using the menu “tools” --> “Serial port”
Select the board type by using “tools” --> “board”

## Slide 7: Arduino Workflow Demo
Click a to compile the source code
Click è to download binary code to the board
Click  to view the output

## Slide 8: Introduce the software architecture
Arduino bootloader
  Communicate with PC to recieve the binary
  Run binary
setup()
  Execute only once
  Do some initialization / Configuration
loop()
  Called repeatly and infinitely
Start
Reset

## Slide 9: Learn Arduino programming skills by examples
Serial Communication
  Serial.begin(9600);
  Serial.println(“some text”);
  Serial.print(“some text”);
  Serial.println();
  Serial.print(somevar);

## Slide 10: Digital I/O
pinMode()
  INPUT/OUTPUT
digitalRead()
  get the pin logical voltage value: HIGH/LOW
digitalWrite()
  set the pin logical voltage value: HIGH/LOW
Logic Level: 0 / 1
  TTL: 0~5V
  CMOS: 0 ~3.3V

## Slide 11: Analog Input / Output
analogRead()
  convert voltage to binary value
  Analog-Digit-Convert (ADC)
analogWrite()
  convert binary value to voltage
  Arduino support only PWM

## Slide 12: What's PWM
The average value of voltage (and current) fed to the load is controlled by turning the switch between supply and load on and off at a fast rate. The longer the switch is on compared to the off periods, the higher the total power supplied to the load

## Slide 13: Time based function
tone()/noTone()
  Generate specified frequency square wave
pulseIn()
  Evalue the time elapsed before the pulse (HIGH or LOW)
millis()
micros()
delay()
delayMicroseconds()

## Slide 14: Demo Program
Ultrasonic distance measurement

## Slide 15: Principle
Distance = 344 x time / 2 meter

## Slide 16: Practice

## Slide 17: 6 Questions?